## Slide 1
Social Event Recommendation Agent
Human-Centered Interaction and Collaboration in Robotics
Final Project Demonstration · 16 July 2026
Sunesh Praveen Raja Sundarasami
Hochschule Bonn-Rhein-Sieg
Advisors
Prof. Dr. Teena Hassan
Ritwik Sinha, M.Sc.

## Slide 2
REQUIREMENTS
1
Detect & verify a face
Haar cascade + 5-frame smoothing detects a face; on-device LBPH verifies it against enrolled group members.
2
Multi-modal greeting, personalized
Three-beat wave / nod / open-arms greeting; personalized by name when the face is recognized (or freshly enrolled with consent).
3
Robust to detection/verification noise
Asymmetric smoothing (4-of-5 to start, 2-of-5 to sustain) and a wide-margin LBPH threshold absorb flicker and misclassification.
4
Conversation to find preferred events
A LangGraph dialogue manager elicits six preferences through open, LLM-framed questions.
5
Internal model + ranked inference
A 3-layer Bayesian network (pyAgrum) infers the best-fit event and ranks all 8 candidates by posterior probability.
6
Illustrative gestures during speech
Every spoken line is paired with a synced gesture: wave, nod, think, present, or a short talk beat for questions.
7
Socially appropriate farewell
A spoken goodbye and wave close the interaction, then the FSM resets cleanly for the next visitor.
8
Filter abusive language
A flagged-word guard declines to parse hostile replies and politely asks the person to rephrase instead.
9
Speech input
Replies can be spoken and transcribed on-device with local Whisper, so no audio leaves the machine.
10
Name + marketing slogan
JARVIS: “At your service. Scanning the local grid for maximum energy signatures.”
Social Event Recommendation Agent
2

## Slide 3
Social Event Recommendation Agent on Pepper: Single-Route Architecture
based on Kopp & Hassan, 2022 (slides 7–8) | red = processing, green = decision, blue = generation, grey = knowledge. The Dialogue stage is the LangGraph (expanded below).
Knowledge & data
Bayesian CPTs from event catalogue ·
8 events + images (imgs/) · schema (contracts.py)
User
face + speech
User
sees + hears
Perception
(sense + recognize)
Face: Haar + 5-frame smoothing
ASR: faster-whisper (local)
or typed text
Interpretation
(understand): LLM
Groq Llama-3.3 service:
frames questions & parses
replies → 6 slots (validated)
Dialogue Manager
(manage turn / select)
FSM 'Conversation' state runs
the LangGraph slot-filling loop
▼ expanded below ▼
Bayesian Reasoning
(decide)
3-layer Bayes net (pyAgrum)
6 evidence → 3 latent → 8 events
ranked events + explanation
Behaviour & Acting
(create + perform)
speech (TTS) + gesture
(wave/nod/think/present)
+ tablet image · Pepper/qiBullet
per turn: Pepper asks (TTS) → user answers (ASR) → repeats until 6 prefs filled
Dialogue Manager: LangGraph (dialogue/graph.py)
runs during the FSM 'Conversation' state · fills the 6 preference slots one at a time, with LLM reframing and conflict handling
START
END
Finish
Router
pick next empty slot
QuestionFramer
ask (LLM-framed),
capture the reply
AnswerParser
reply → candidate
evidence (LLM)
ConflictResolver
spot contradictions,
re-open the slot
Evaluator
commit / reframe /
default
missing
no conflict
all slots filled
conflict → ask either/or
answer not usable → reframe
usable / committed / default → next slot
↑ question out via Behaviour-TTS · answer in via Perception-ASR
↑ uses Interpretation-LLM
Finish → returns the 6-slot evidence to the FSM → Bayesian Reasoning (above)
Single route: perception → interpretation → dialogue (LangGraph, looping per turn) → Bayesian reasoning → behaviour → Pepper. One recommendation is reasoned once all 6 preferences are gathered.

## Slide 4
DEMO
1
IDLE
Watches for a face held stable across a 5-frame window.
2
GREETING
Identifies or enrolls the visitor, then waves and introduces itself.
3
CONVERSATION
LangGraph fills 6 evidence slots: Budget, Group, Activity, Setting, Time, Interest.
4
REASONING
Bayesian network turns evidence into 3 latent factors, then ranks 8 event types.
5
RECOMMENDATION
Shows the top event on the tablet and explains why it fits.
6
FAREWELL
Says goodbye, then resets to Idle once the visitor leaves.
RUN IT (src/main.py)
--source
webcam · pepper · hybrid
where faces come from / whether Pepper is spawned in qiBullet
--answer
text · speech
typed replies vs. spoken, transcribed on-device by local Whisper
Optional: pre-enroll a face offline
uv run python src/enroll_face.py --name Alex
Full pipeline used in the live demo:
uv run python src/main.py --source hybrid --dialogue real --answer speech
SAMPLE EXCHANGE
JARVIS: I don't think we've met yet. What's your name?
You: Alex
JARVIS: Nice to meet you, Alex. Mind if I remember your face?
You: yes (captures ~15 samples, retrains)
JARVIS: Great, I'll remember you next time, Alex! (wave · nod)
…….
JARVIS: Based on what you told me:
1. Museum (34%) 2. Workshop (19%) 3. Food (15%)
JARVIS: I suggest Museum, since a cultural, low-key venue fits what you told me.
If Alex declines, or is already known: the greeting adapts immediately, with no enrollment step.
Social Event Recommendation Agent
4

## Slide 5
TECHNICAL CHALLENGES
1
Two incompatible Python versions
qiBullet/NAOqi needs Python 3.8; LangGraph needs ≥ 3.9
Bridged by running the dialogue side as its own OS process, over stdin/stdout
2
Local models tested, cloud model used
Tried local models sized for 6 GB VRAM: Llama 3.2 3B, Phi-3.5-mini, Qwen2.5-7B (4-bit)
Groq's cloud Llama 3.3 was faster and sharper; only speech-to-text stayed local
3
Gesture timing matched to speech length
Gestures run on their own thread, timed to speech
The ~3.2 s open_arms swing didn't fit variable-length LLM questions
Shortened to a ~1.25 s “talk” beat for conversation turns
4
Face recognition can misidentify people
An unenrolled friend was usually flagged as unrecognized
But was occasionally greeted as “Sunesh” anyway
Wide LBPH margin (~0 vs. ~180) helps, but doesn't guarantee zero false positives
5
Fitting speech recognition on a 6 GB GPU
large-v3 in int8_float16 needs ~2.2 GB, vs. 3.4 GB at float16
Fits comfortably on a 6 GB card
Took manual setup to get GPU drivers working on Windows
6
Keeping the event image aligned with the tablet
qiBullet exposes the Tablet_frame link, but no tablet API
A thin textured panel re-positions from live forward-kinematics every 30 ms
Offset to sit in front of the built-in screen, not behind it
Social Event Recommendation Agent
5

## Slide 6
ETHICAL CONCERNS
1
Biometric data, only with consent
JARVIS asks first: a name, then “would it be okay if I remember your face?”
Declining is honoured; nothing is captured
Accepted photos stay local under known_faces/, git-ignored
2
No delete option for enrolled faces
Enrollment is opt-in, but there's no way to ask JARVIS to delete photos afterward
Removing yourself today means manually deleting a folder
3
Always-on camera, before consent applies
Idle continuously watches for a face before any interaction starts
Consent only ever covers what happens after that point, not the watching itself
4
Conversation still leaves the device
Parsed preference text is still sent to Groq's cloud LLM
Only voice audio (local Whisper) and face photos (local LBPH) stay on-device
5
Personalization raises the trust stakes
Being remembered by name and face makes JARVIS feel less like a generic greeter
That warmth makes it easy to forget its picks are just ranked guesses, not judgments from someone who knows you
6
The abuse filter is a simple word list
Just a short list of flagged words: cheap and easy to explain
Won't catch hostility phrased differently, a conscious trade-off for simplicity
Social Event Recommendation Agent
6

## Slide 7
Thank you
Social Event Recommendation Agent
Sunesh Praveen Raja Sundarasami
Questions welcome.